JUMA-TRX2 Boot loader OH2NLT / 06.07.2007

# General

JUMA Boot loader is a piece of software programmed into the dsPIC30F6014A flash. Boot loader allows user  to upgrade (download) new or modified JUMA-TRX2 control program into the dsPIC30F6014A flash memory without any special tools. Control program or firmware is transferred thru JUMA-TRX2 RS232 port. Only PC computer with serial port and Ingenia boot loader PC side program is needed.

# How it operates

Boot loader is two part program. Client part is programmed into the JUMA-TRX2 control processor (dsPIC30F6014A) memory top part and PC side user interface program (GUI). Every time JUMA-TRX2 is started(power on) control is given to this code. Boot loader code checks if VFO button is held down during start up. VFO button pressed during start is signal for the boot loader to start the download procedure. Message is written into the TRX2 LCD display and boot loader starts to negotiate PC connection. If connection is not established within about four seconds boot loader starts JUMA-TRX2 control program. Start without VFO button pressed transfers control immediately to TRX2 control program. PC side program (GUI) is started after JUMA-TRX2 boot loader is running. Successful communications between PC and JUMA-TRX2 is indicated on PC screen. After this phase user can select firmware file (juma-trx2.hex) for downloading (Flash programming) and start programming cycle. This procedure is explained in a excellent way in Ingenia documentation.

Some details

If you are compiling your own firmware for JUMA-TRX2 special linking loader script for Microchip C30 compiler should be used. There must always be jump to user code start at absolute program memory address 0x100.

.text __CODE_BASE :

{

/*

** Generate extra goto __reset for boot loader. OH2NLT 050106

** Boot loader allways jump to start address 0x100

*/

SHORT(ABSOLUTE(__reset));

SHORT(0x04);

SHORT((ABSOLUTE(__reset) >> 16) & 0x7F);

SHORT(0);

*(.handle);

*(.libc) *(.libm) *(.libdsp);  /* keep together in this order */

*(.lib*);

*(.text);

} >program

For more details see provided JUMA-TRX2 source code and Mplab project files.

Preparations for loading firmware

Get PC with XP operating system and serial port.

Get D9 male-Female serial cable. At least pins 2,3,5 must be connected 1:1

Get Ingenia and install PC client software to your PC. Follow Ingenia instructions.

Ingenia dsPICbootloader PC software can be downloaded from Ingenia www site.

http://www.ingenia-cat.com/es/downloads.php

!!! IMPORTANT !!!

After installing Ingenia bootloader you must copy THIS FILE over the original ibl_dspiclist. Original file does not contain definitions for dsPIC30F6014A and do not work with JUMA-TRX2.

Get JUMA-TRX2 firmware image (juma-trx2_Vxxx.hex) what you like to download into your JUMA-TRX2. Example juma-trx2.hex

Instructions

Read Ingenia boot loader instructions.

Start Ingenia GUI at PC. Hyper Terminal or any other program must not be running (reserving the com port). JUMA-TRX2 must be switched off.

Configure PC com port if neded. Boot loader default baud rate is 115200.

Press configuration done. Now PC software waits JUMA-TRX2  Flash Writer to be started.

Start(power on)  JUMA-TRX2 keeping VFO button pressed. You should see text in LCD display:

JUMA-TRX2 Flash

Writer started..

Successful communication between PC software and JUMA-TRX2 brings above screen visible.

Next point and click open HEX file. Select .hex file from your local disc (for example juma-trx2.hex).

After successful selection of hex file start write button appears. Start transfer / flash programming. This should take about 10s.

After successful programming you should disconnect power from power supply.  JUMA-TRX2 PWR button does not work in this state.

How to test serial port

Start Hyperterminal or any other terminal program in your PC. Configure used com port 9600-8-N. Connect RS232 cable to JUMA-TRX2. Power up JUMA-TRX2 (normal power on start). You should see following text at terminal screen:

Select RS232 = Test from juma TRX2 display setup. Now you can try few test commands from terminal.

I (capital I) should print software version

E(capital e) should dump JUMA-TRX2 configuration EEPROM content

Other commands. See JUMA-TRX2 user manual and software source code listing.

Boot loader software

JUMA-TRX2 boot loader

You need this if you have “empty” dsPIC30F6014A chip. Boot loader is programmed into the dsPIC chip with Mplab ICD tool or equivalent programmer. Boot loader code is based on Ingenia dsPIC bootloader firmware but modified for JUMA-TRX2 hardware and usage. When programming “empty” dsPIC30F6014A chip you should keep Power button pressed all the time or install Jxx in the DDS board to keep power on during programming. JUMA-TRX2 Power switch is software controlled.

Backup copy of Ingenia PC client software

If Ingenia www site is unreachable you can find PC side software also from here.

Ibl_dspiclist.xml file containing dsPIC30F6014A definitions.

Other

You can of course program JUMA-TRX2 firmware with Microchip ICD 2 tool or other programmer without boot loader. However if you do this boot loader is erased from dsPIC30F6014A flash memory and must be reprogrammed if needed later.

For initial loads I have also made special .hex file containing both boot loader firmware and JUMA-TRX2 firmware v1.00. This file can be found from here.

* end *